## Slide 1: Multipath Traffic Engineering
Kireeti Kompella
Chief Engineer & SVP, AWAN

## Slide 2
Agenda
Goals of Traffic Management
  Why/why not Engineer Traffic?
MPLS TE in 1998 and today
Tools at Our Disposal
  ECMP
  Traditional TE
  Multipath TE
Conclusion

## Slide 3
Goals of Traffic Management
Meet customer requirements
Handle (temporary) traffic surges
Flash crowds
Elephant flows
Build new capacity for future growth
Optimize use of existing capacity
Reserve/ use case
Reserve/ customer
Plan for link/node outages, maintenance
SRLG
undersea
Measure, measure, measure!
Avoid certain links, nodes, paths for sensitive data
No MACsec
geo-political
node fails trust
Multi-ingress/multi-egress traffic

## Slide 4: Why Engineer Traffic?
To better utilize network capacity
To handle faults and network outages
To improve (end) customer experience
To get more insights into network traffic patterns
Why Not Engineer?
Throw bandwidth at the problem!
Use ECMP and cross fingers!
They don’t pay us differentially!
Patterns? What patterns?
The biggest concerns about TE are 1) the OPEX overhead of “babysitting” LSPs and 2) scaling

## Slide 5: MPLS Traffic Engineering in 1998
When MPLS was introduced at the IETF, an important goal was Traffic Engineering
RFC 2702: Requirements for Traffic Engineering over MPLS (1998)
Bringing these requirements to a product was my first task in routing protocols – 27 years ago
A few key things changed over that span of time, but the fundamentals remained the same
Coming back to this subject after all our experience allows new perspectives on load balancing & TE …
… perhaps brings something novel to the table
These issues seem to be very timely, and could change the way we engineer networks, especially for AI clusters and DCI complexes
“Auto-bandwidth” was a big step forward, making bandwidth specs easier and more useful
The notion of "forwarding adjacencies" allowed us to more easily build hierarchical TE

## Slide 6: Traffic Management Today
Edge inferencing will require fast response
Management and automation tools have vastly improved
01
Increased focus on costs (CAPEX and OPEX) and revenues (ARPU)
02
Control/data planes handle scale & churn much better
03
Telemetry, analysis, insights are HUGE today (and necessary for AIOps)
04
Customer demands, requirements are stricter
Network usage is changing  new traffic patterns

## Slide 7: ECMP “versus” TE: a false dichotomy
Equal cost multipath: easy, nice features, no signaling
Traffic engineering: not quite as easy, many more features, requires signaling

## Slide 8
Tools for Traffic Management:
1. Equal cost multipath

## Slide 9: Equal-cost multipath routing
N
packet arrives
Pick one of many next hops with equal cost to destination
(dest-based forwarding)
Can this cause routing loops?
No, not if all nodes have the same view of the topology and compute shortest paths
This is what IGPs do

## Slide 10: Dijkstra’s shortest path algorithm
“20-minute invention” while sipping coffee
  (Directed) graph with positive weights on the edges
  Works to find one shortest path from one node (“ingress”) to another node (“egress”)
  Equal time complexity to find all shortest paths to the egress
Simple, elegant, efficient
  O((|E| +|V|) log(|V|) or O(|E| + |V| log(|V|)), depending on the type of heap you use
Provably correct
  Simple proof by induction
Greediness works (in this case) 
Each node can independently compute its paths to the egress and forwarding WILL NOT LOOP

## Slide 11: Benefits: let’s look at node N
N
Traffic surge
No one next hop will see entire surge
(unless you have a seriously fat flow!)
Link fails: remaining next hops will take on traffic

## Slide 12: Downsides
N
Traffic
What ratios should be used across these next hops? What about next next hops and beyond?
Link fails:
now what?
Simply sending traffic back from where it came (previous hop) WILL cause looping. Solvable, but no longer simple, and may need signaling
All that said, shortest path routing with ECMP is very nice, and used quite a lot
Suppose N has a single next hop

## Slide 13: Clos network (say, for a machine-learning cluster) (epitome of ECMP networks!)
Very structured network
(“network engineering”)
As symmetric as possible
SS1
SS3
SS2
S1
S2
S3
L1
L2
L4
L3
…
All links between nodes SSm and Sn are of equal length and of the same capacity
Similarly for links between Sn and Lk

## Slide 14
Tools for Traffic Management:
2. Traditional Traffic Engineering

## Slide 15: Define “constraints” and find a “feasible” path
A
Z
Find a path from A to Z that can carry 20G, goes over “green” links, and avoids “insecure” links
N
(The network operator defines what “green” and “insecure” means.)
Transit node N has no idea of the path constraints, so it needs to be told how to forward – via signaling
RFC 2702 defines traffic engineering constraints, and RFC 3209 defines signaling for TE paths
IGP extensions distribute link and node properties so that A can compute a “feasible” path to Z
Notes: Feel free to tune out

## Slide 16: If a link fails, N can compute a “detour” for the link
A
Z
N
M
X
P
P is a “downstream” node on the path to Z
The path from N to P is also signaled. In particular, it can avoid “shared risk” with the failed link and node M

## Slide 17: TE has seen good (but far from universal) deployment
The ability to set up protection paths has been a prominent TE use case
Bandwidth reservations (and a relatively new feature, “auto-bandwidth”) also see a lot of usage
Having state from ingress to egress allows the operator to create an accurate traffic matrix across all such pairs
On the flip side, there are those who prefer to “throw bandwidth at the problem” (CapEx vs OpEx)
Some network operators desire TE, but don’t want to give up the benefits of ECMP
There are (valid) concerns about state (and churn) in the network using TE
If you are in this last category, keep listening
Another use case is automated congestion avoidance using telemetry and re-computation

## Slide 18
New Tool for Traffic Management:
3. Multipath Traffic Engineering

## Slide 19: Shortest Path Routing
400G link
800G link
All link metrics are equal
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
Can only send a maximum of 400 Gbps from R1 to R12!

## Slide 20: Conventional TE
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
Can achieve 1600 Gbps throughput from R1 to R12.
But require four LSPs (manually created or via TE++) to do so.
400G
400G
400G
400G

## Slide 21: Multipath TE (MPTE)
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
1600 Gbps throughput is achieved with just one MPTE LSP.
LSP (MPTE DAG) can branch (with any desired split ratio) and recombine
25%
25%
50%
50%
50%
X%
= the local split percentage at a junction node

## Slide 22: MPTE and link failure
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
Automatic adjustment of the MPTE LSP and its branching ratios if the topology changes (e.g. due to link failure)
33.3%
33.3%
33.3%
X%
= the local split percentage at a junction node

## Slide 23: MPTE with constraints
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
33.3%
66.6%
50%
50%
X%
= the local split percentage at a junction node
Can have constraints, just like with conventional TE
E.g. “exclude links with purple admin-group”

## Slide 24: MPTE with multiple egresses
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
Can have multiple egress PEs for the same MPTE DAG!
Note: this is not a multicast P2MP LSP: traffic is load-balanced across the egress PEs.
25%
25%
50%
50%
50%
R15
50%
50%
50%
50%
X%
= the local split percentage at a junction node
50%
50%
50%
50%
Suppose R15 is “as good as” R12 as an egress.
R15 can be accommodated by the MPTE DAG with relatively little extra state

## Slide 25: Back to our machine-learning cluster
The network has been purpose-engineered for ECMP. Can traffic engineering also help?
SS1
SS3
SS2
S1
S2
S3
L1
L2
L4
L3
…
YES, if the cluster is split among multiple ML inference workloads
NO, if the entire cluster is working on a single giant (LLM?) training task
COLOR the routers and CPUs/GPUs, and reserve resources appropriately
Even a network engineered for ECMP can benefit from multipath TE (but not from single-path TE!)

## Slide 26
Conclusion

## Slide 27: Key takeaways
You can meaningfully add multipath to Traffic Engineering, getting the best of both worlds
You can meaningfully add Traffic Engineering to a network engineered for ECMP, and get new value
Both paths lead to Multipath Traffic Engineering (MPTE)
With the lessons learned from hard-earned experience, we can build a much more robust and scalable protocol for MPTE
My goal is to make you (re)consider TE. Hopefully, I’ve accomplished that 

## Slide 28: Further information
IETF draft:
  https://datatracker.ietf.org/doc/draft-kompella-teas-mpte/
  More drafts to come on signaling and PCEP details, as well as YANG models
Recording of MPTE presentation at MPLS World Congress
  https://player.vimeo.com/video/1069205740?autoplay=1