## Slide 1: Multipath Traffic Engineering MPTE
Kireeti Kompella
Chief Engineer and SVP, Routing Infrastructure Solutions
HPE Networking

## Slide 2
Multipath Traffic Engineering (MPTE)
  Adding Multipath to TE
  Adding TE to Multipath
  MPTE CLI
  MPTE RSVP
Takeaways and References

## Slide 3
Multipath Traffic Engineering MPTE
Adding Multipath to TE

## Slide 4: Shortest Path Routing (No TE)
400G link
800G link
All link metrics are equal
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
Can send a maximum of 400 Gbps from R1 to R12 using a single path
Can send a maximum of 1200 Gbps from R1 to R12 using a DAG with equally-weighted load balancing at R2 without congestion (800Gbps links are underutilized)

## Slide 5: Conventional TE
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
400G
400G
400G
400G
Can achieve 1600 Gbps throughput from R1 to R12
But this requires four LSP constructs (manually created or created via TE++) to do so

## Slide 6: Multipath TE (MPTE)
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
25%
25%
50%
50%
50%
X%
Local split percentage (load –share) at a junction node
1600 Gbps throughput is achieved with just one MPTE DAG construct
MPTE DAG can branch (with an “optimal” split ratio at each junction) and recombine as needed

## Slide 7: MPTE and Link Failure
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
33.3%
33.3%
33.3%
Automatic adjustment of the MPTE DAG and its branching ratios when a link on the DAG goes down temporarily.
100%
0%
Shape of the DAG remains unchanged unless there is a permanent change to the topology (reduces DAG churn)
Still in DAG!

## Slide 8: MPTE with Constraints
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
33.3%
66.6%
50%
50%
Can have constraints, just like with conventional TE
E.g. “exclude links with purple admin-group”
X%
Local split percentage (load –share) at a junction node

## Slide 9: MPTE with Multiple Egresses
400G link
800G link
R1
R2
R3
R5
R4
R6
R7
R8
R9
R10
R11
R12
25%
25%
50%
50%
50%
R15
50%
50%
50%
50%
50%
50%
50%
50%
Can have multiple egress PEs for the same MPTE DAG!
Note: this is not a multicast P2MP LSP: traffic is load-balanced across the egress PEs.
R15 can be accommodated by the MPTE DAG with relatively little extra state
(only R11, R8, R5 and R6 have updated state (more nhops); rest of DAG is unchanged)
Suppose R15 is “as good as” R12 as an egress (e.g., iBGP multipath; VPN multihoming)

## Slide 10: MPTE DAG: 3.2T AI Training Corridor
Ingress (AI Cluster A)
Egress (AI Cluster B)
R2
R3
R5
R6
R7
R8
R9
R10
R11
R12
1.6 Tbps
R13
1.6 Tbps
25%
25%
50%
50%
50%
33%
67%
Architecture based on draft-kompella-teas-mpte | RSVP-TE extensions: draft-kbr-teas-mptersvp.
Single MPTE tunnel (= DAG with TE constraints + weighted LB) with dual ingress & egress
Note: ingress of tunnel is egress from Cluster A; egress of tunnel is ingress into Cluster B
X%
Local split ratio at junction
50%
R4
25%
25%
Selected DAG links
Excluded by constraint
50%
50%
AI Cluster B
How It Works
Traffic enters at R0 and R1 (ingresses) and is distributed across weighted next-hops toward R12 and R13 (egresses).
Constraint: 1.6Tbps at each ingress + avoid links with RED affinity
Built-in Resiliency
Multiple next-hops at most junctions. On failure, rebalance traffic across surviving next-hops immediately (Fast Re-Route). Re-signaling is global repair
Multi-Ingress, Multi-Egress
R0 and R1 serve as ingress PEs;
R12 and R13 serve as egress PEs
AI Cluster A
1.6 Tbps
R1
R0
1.6 Tbps

## Slide 11
Multipath Traffic Engineering MPTE
Adding TE to Multipath

## Slide 12: Clos Network – For a Machine-Learning Cluster (Epitome of Multipath Networks!)
Very structured network:
as symmetric as possible
SS1
SS3
SS2
S1
S2
S3
L1
L2
L4
L3
…
All links between nodes SSm and Sn are of equal length and of the same capacity
Similarly for links between Sn and Lk
Superspine
Spine
Leaf
Equally weighted multipath

## Slide 13: Adding TE to the ML cluster
The network has been purpose-engineered for ECMP. Can traffic engineering also help?
SS1
SS3
SS2
S1
S2
S3
L1
L2
L4
L3
…
YES, if the cluster is split among multiple ML inference tasks
NO, if the entire cluster is working on a single training task
COLOR CPUs/GPUs/ network and reserve resources by task
Even a network engineered for ECMP can benefit from multipath TE
No longer equally weighted multipath
“Blue” bandwidth & weights depend on “Blue” workload
Non-multipath TE is a total non-starter in ML clusters!

## Slide 14: MPTE is Topology-Independent
Fat trees (Clos architecture) have been the dominant topology for DC networks for several decades
However, they are very fat (need lots of switches, links, optics, fiber, power, cooling, …)
New topologies have recently been proposed:
  Rail-only topology (MIT, https://people.csail.mit.edu/ghobadi/papers/rail_only_hoti_2024.pdf)
  Resilient Network Graphs (AWS, https://arxiv.org/pdf/2604.15261)
MPTE works efficiently in both the Rail-only and RNG topologies, as well as the original Clos topology
Fresh off the press:
https://tedigest.com/2026/06/24/the-growing-need-for-traffic-engineering-in-datacenter-fabrics/

## Slide 15
MPTE CLI commands
(work in progress)

## Slide 16: MPTE Tunnel Configuration
root@R1_re# set protocols mpte tunnel 1to9 ?
Possible completions:
> admin-group Administrative group policy
> admin-group-extended Extended administrative group policy
compute-engine Compute engine address
compute-only Compute DAG only, do not signal tunnel
description Text description of tunnel
disable Disable tunnel
+ egress Tunnel egress address
> hop Hop constraints configuration
> ingress Tunnel ingress configuration
max-jcts Maximum number of junctions (1..255)
max-nhops Maximum number of nexthops per junction (1..255)
min-nhops Minimum number of nexthops per junction (1..255)
> optimize Optimization configuration
originator Tunnel originator address
priority Preemption priorities
signaling-source Signaling source address
signaling-type Signaling protocol type
type Tunnel type
root@R1_re# set protocols mpte tunnel 1to9 optimize ?
Possible completions:
delay Delay metric optimization
igp IGP metric optimization
metric-margin Metric margin for path selection (0..4294967295)
te Traffic engineering metric optimization
root@R1_re# set protocols mpte tunnel 1to9 hop ?
Possible completions:
minimum-bandwidth Minimum bandwidth per hop (bps)
Control the span of the DAG

## Slide 17: show mpte tunnel terse
Total: 1
Up 1, Degraded 0, Down 0
show mpte tunnel brief
Originator ID State JCTs Type SigType TunnelName
1.1.1.1 1 Up 100% 8 MPLS-Sig RSVP SFO_IAD_Gold_001
Total: 1
Up 1, Degraded 0, Down 0

## Slide 18: show mpte tunnel detail
SFO_IAD_Gold_001, Originator: 1.1.1.1, ID: 1
Up, Availability: 100%, Type: MPLS-SigLabels
ComputeEngine: 1.1.1.1
SignalingSource: 1.1.1.1, SignalingType: RSVP
Ingresses (1):
1.1.1.1, BW 18G
Egresses (1):
4.4.4.4
OptimizationObjective: TE, Slack: Infinite
DAGVersion 1
Affinities:
IncludeAny: Gold
Priorities: 7 0
Junctions (4):
JCT 1.1.1.1, Up, ReqBW 18G, MTU 9500
NHOPs (4):
NHOP 10.1.12.2 Idx 0x201
HopVersion 1, Up, OutLabel: 2001
LoadShare 1, ResBW 3G
NHOP 10.1.12.4 Idx 0x202
HopVersion 1, Up, OutLabel: 2002
LoadShare 1, ResBW 3G
NHOP 10.1.13.2 Idx 0x301
HopVersion 1, Up, OutLabel: 3001
LoadShare 2, ResBW 6G
…
…
NHOP 10.1.14.2 Idx 0x401
HopVersion 1, Up, OutLabel 4001
LoadShare 2, ResBW 6G
JCT 2.2.2.2, Up, ReqBW 6G, MTU 9500
PHOPs (2):
PHOP 10.1.12.1 Idx 0x101
HopVersion 1, Up, InLabel: 2001
PHOP 10.1.12.3 Idx 0x102
HopVersion 1, Up, InLabel: 2002
NHOPs (3):
NHOP 10.1.24.2 Idx 0x402
HopVersion 1, Up, OutLabel: 4002
LoadShare 1, ResBW 1G
NHOP 10.1.24.4 Idx 0x403
HopVersion 1, Up, OutLabel: 4003
LoadShare 1, ResBW 1G
NHOP 10.1.23.2 Idx 0x302
HopVersion 1, Up, OutLabel: 3002
LoadShare 4, ResBW 4G
JCT 3.3.3.3, Up, ReqBW 10G, MTU 9500
PHOPs (2):
PHOP 10.1.13.1 Idx 0x103
HopVersion 1, Up, InLabel: 3001
PHOP 10.1.23.1 Idx 0x203
HopVersion 1, Up, InLabel: 3002
…
…
NHOPs (1):
NHOP 10.1.34.1 Idx 0x404
HopVersion 1, Up, OutLabel: 4004
LoadShare 1, ResBW 10G
JCT 4.4.4.4, Up, ReqBW 18G, MTU –
PHOPs (4):
PHOP 10.1.14.1 Idx 0x104
HopVersion 1, Up, InLabel: 4001
PHOP 10.1.24.1 Idx 0x204
HopVersion 1, Up, InLabel: 4002
PHOP 10.1.24.3 Idx 0x205
HopVersion 1, Up, InLabel: 4003
PHOP 10.1.34.1 Idx 0x303
HopVersion 1, Up, InLabel: 4004

## Slide 19: show mpte tunnel extensive
SFO_IAD_Gold_001, Originator: 1.1.1.1, ID: 1
Up, Availability: 100%, Type: MPLS-SigLabels
ComputeEngine: 1.1.1.1
SignalingSource: 1.1.1.1, SignalingType: RSVP
Ingresses (1):
1.1.1.1, BW 18G
Egresses (1):
4.4.4.4
OptimizationObjective: TE, Slack: Infinite
DAGVersion 1
Affinities:
IncludeAny: Gold
Priorities: 7 0
Junctions (4):
JCT 1.1.1.1, Up, ReqBW 18G, MTU 9500
NHOPs (4):
NHOP 10.1.12.2 Idx 0x201
HopVersion 1, Up, OutLabel: 2001
LoadShare 1, ResBW 3G
NHOP 10.1.12.4 Idx 0x202
HopVersion 1, Up, OutLabel: 2002
LoadShare 1, ResBW 3G
NHOP 10.1.13.2 Idx 0x301
HopVersion 1, Up, OutLabel: 3001
LoadShare 2, ResBW 6G
…
…
NHOP 10.1.14.2 Idx 0x401
HopVersion 1, Up, OutLabel 4001
LoadShare 2, ResBW 6G
JCT 2.2.2.2, Up, ReqBW 6G, MTU 9500
PHOPs (2):
PHOP 10.1.12.1 Idx 0x101
HopVersion 1, Up, InLabel: 2001
PHOP 10.1.12.3 Idx 0x102
Version 1, Up, InLabel: 2002
NHOPs (3):
NHOP 10.1.24.2 Idx 0x402
HopVersion 1, Up, OutLabel: 4002
LoadShare 1, ResBW 1G
NHOP 10.1.24.4 Idx 0x403
HopVersion 1, Up, OutLabel: 4003
LoadShare 1, ResBW 1G
NHOP 10.1.23.2 Idx 0x302
HopVersion 1, Up, OutLabel: 3002
LoadShare 4, ResBW 4G
JCT 3.3.3.3, Up, ReqBW 10G, MTU 9500
PHOPs (2):
PHOP 10.1.13.1 Idx 0x103
HopVersion 1, Up, InLabel: 3001
PHOP 10.1.23.1 Idx 0x203
HopVersion 1, Up, InLabel: 3002
…
…
NHOPs (1):
NHOP 10.1.34.1 Idx 0x404
HopVersion 1, Up, OutLabel: 4004
LoadShare 1, ResBW 10G
JCT 4.4.4.4, Up, ReqBW 18G, MTU –
PHOPs (4):
PHOP 10.1.14.1 Idx 0x104
HopVersion 1, Up, InLabel: 4001
PHOP 10.1.24.1 Idx 0x204
HopVersion 1, Up, InLabel: 4002
PHOP 10.1.24.3 Idx 0x205
HopVersion 1, Up, InLabel: 4003
PHOP 10.1.34.1 Idx 0x303
HopVersion 1, Up, InLabel: 4004
7 Feb 5 01:19:51.998 Up 100%
6 Feb 5 01:19:51.975 1.1.1.1: Local Junction Up
5 Feb 5 01:19:51.956 2.2.2.2: Junction Up
4 Feb 5 01:19:51.945 3.3.3.3: Junction Up
3 Feb 5 01:19:51.875 4.4.4.4: Junction Up
2 Feb 5 01:19:50.945 CSPF: Computation Result Accepted – 4 junctions, 8 TE links
1 Feb 5 01:19:50.845 Originate DAG Version 1

## Slide 20
MPTE RSVP

## Slide 21: Why use RSVP to provision MPTE state?
It is THE Resource Reservation Protocol (duh!)
  MPTE Tunnel is a bandwidth engineering construct which requires resources to be reserved
Facilitates ordered admission control and priority-based preemption
Facilitates automatic update of link state resource reservation
Facilitates ordered programming of labeled routes
  Facilitates ordered addition/deletion/modification of route next-hops
Provides an option to incrementally deploy MPTE tunnels
  Interoperate with traditional RSVP signaling procedures
Facilitates seamless use of signaled MPLS label switching
  No special “label management” policies required
Facilitates distributed provisioning of MPTE tunnels

## Slide 22: Optimized Signaling Procedures – Design Guidelines
Minimize “Refresh” message processing
  Refresh-interval independent RSVP [RFC8370] procedures are always ON
Avoid unnecessary signaling adjacency failures
  Relaxed hello-interval by default
Minimize the number of signaling notifications triggered when a link fails/degrades
  Resource Notifications are always ON
    No per-state notifications sent when a topological-element goes down or gets degraded
Minimize “Trigger” message processing
  Signaling-Source sends PATH message (JUNCTION state setup/update) directly to the junction
    No hop-by-hop PATH signaling
  Avoid unnecessary junction state updates
    Sub-Graph only updates MUST be accommodated

## Slide 23: RSVP Signaling Messages for Junction Management
(Signaling) Source to Junction (S2J) Messages
  JunctionCreate
    RSVP MPTE Path
  JunctionUpdate
    RSVP MPTE Path
  JunctionDelete
    RSVP MPTE PathTear (with or without CONDITIONS object)
Junction to Junction (J2J) Messages
  Upstream (J2JU) Messages
    JunctionNextHopReservation
      RSVP MPTE Resv
    JunctionDown
      RSVP MPTE Notify
  Downstream (J2JD) Messages
    JunctionDelete – Conditional
      RSVP MPTE PathTear (with CONDITIONS object)
    JunctionNotReady
      RSVP MPTE ResvErr
Junction to Source (J2S) Messages
  JunctionNotify
    RSVP MPTE Notify
  ResourceNotify
    RSVP Rsrc Notify

## Slide 24: Initial Setup Sequence
R1
R2
R3
R4
R7
R5
R6
R8
Initiation of setup sequence on MPTE tunnel signaling source, R1:
  R1 sends an M-Path message to each junction node (R2, R3, R4, R5, R6, R7, and R8)
  R1 processes the ingress JUNCTION, constructs a JSB, and waits for an M-Resv message to arrive from each JCT-NHOP (R2 and R3).
MPTE Tunnel R1toR8
Signaling Source: 1
M-Resv message processing on transit junction nodes (R2, R3, R4, R5, R6, R7):
  Each transit junction node waits until M-Resv messages are received from all available JCT-NHOPs and then:
    Updates BW reservation on TE-links.
    Allocates a label for each JCT-PHOP and programs the corresponding labeled route.
    Sends an M-Resv message to each JCT-PHOP with the corresponding allocated label.
    Sends an M-Notify message to R1, indicating that the junction processing is complete on the node.
M-Resv message processing on ingress junction node, R1:
  R1 waits until M-Resv messages are received from all JCT-NHOPs (R2 and R3) and then:
    Updates BW reservation on TE-links.
    Programs a route for the MPTE tunnel.
    Notifies the signaling source (itself) that the junction processing is complete on the ingress node.
Metric on links 2-4, 4-5,3-4 and 4-7 is 10; Metric on 4-6 and 6-8 is 15; Metric on all other links is 20
JBW 6G
JBW 3G
JBW 3G
JBW 2.5G
JBW 3G
JBW 2.5G
JBW 1G
JBW 6G
M-Path message processing on transit junction nodes (R2, R3, R4, R5, R6, R7):
  Each transit junction node processes the JUNCTION, constructs a JSB, and waits for an M-Resv message to arrive from each JCT- NHOP.
M-Path message processing on egress junction node, R8:
  R8 processes the JUNCTION and constructs a JSB.
  R8 sends an M-Resv message to each JCT-PHOP (R5, R6, and R7) with IMPLICIT NULL Label (3).
  R8 sends an M-Notify message to R1, indicating that the junction processing is complete at R8.
M-Notify message processing on the signaling source:
  The signaling source (R1) considers the setup sequence complete when confirmation of junction provisioning is received from all junctions.

## Slide 25
Takeaways

## Slide 26: Summary of Operation
MPTE Tunnel Originator (TO)
User specifies intent:
Ingresses
Egresses
Incoming bandwidth at each ingress
Constraints and Optimization Objective
MPTE Computer (MC)
MC computes the DAG:
Input: specified constraints and optimization objective
Result: an unordered list of junctions (to be sent to the Signaling Source)
MPTE Signaling Source (SS)
SS provisions the MPTE junction state:
Sends signaling messages to each junction node
When all junctions are provisioned, SS declares the tunnel ready for traffic
Ingresses can then start using the MPTE tunnel

## Slide 27: Signaling Options
Protocol choices across deployment environments
WAN/DCI
DC
Hyper Scalars
Topology
IGP
BGP-LS
Own
Signaling
RSVP-TE / PCE
BGP (new AFI/SAFI)
YANG + API
Data Plane
MPLS or IP
IP tunnels*
IP tunnels*
⚡ Initial prototype uses RSVP-TE (proven deployment record)
Other prototypes using gRPC and BGP are currently underway
MPTE · Multipath Traffic Engineering · Signaling Options

## Slide 28: MPTE – Key Differentiators / Attributes
Facilitates optimized (unequally-weighted) load balancing at every junction on the DAG
  Not just on ingress
Amount of churn after a resource-failure/resource-degradation/traffic-demand-change event is significantly less
  Shape of the DAG is largely static post setup
    No unnecessary addition/deletion of routes or next-hops
  Automatic adjustment of junction bandwidth and next-hop load-share
Supports multiple ingresses and multiple egresses
Multipath spread is maximized in the provisioned DAG within practical constraints
Amount of state needed to setup the DAG is significantly less
  Setup junction state at each node on the DAG (as opposed to setting up path state)

## Slide 29: References
https://datatracker.ietf.org/doc/draft-kompella-teas-mpte/
https://datatracker.ietf.org/doc/draft-kbr-teas-mptersvp/
https://datatracker.ietf.org/doc/draft-zzhang-idr-mpte-signaling/
https://datatracker.ietf.org/doc/draft-beeram-pce-pcep-mpted/
https://datatracker.ietf.org/doc/draft-beeram-teas-yang-mpted/
https://www.linkedin.com/pulse/multipath-traffic-engineering-kireeti-kompella-ckupe/