## Slide 1: The TCP Authentication Option (TCP-AO)
September 2020
Ron Bonica

## Slide 2: Motivation
What are we protecting?
  Long-lived TCP sessions
  Examples
    Routing protocols (BGP, LDP)
    Long-lived TCP sessions between other applications
What are we protecting against?
  Blind insertion attacks
  Replay attacks

## Slide 3: Blind insertion Attack on A BGP session
Router A maintains a BGP session with Router B
  They exchange many routes over many hours
Node C sends a few packets per second to Router B for many hours
  IP source address: Router A (spoofed)
  Payload: TCP
    RST bit set
    Source and destination ports: BGP (179)
    Random sequence numbers
B discards most packets, because their sequence numbers are invalid
Sooner or later, C sends a packet with a valid sequence number
BGP session resets

## Slide 4: Legacy Solution: TCP-MD5 [RFC 2385]
Sending and receiving nodes are configured with a pre-shared key
Sending node procedures
  Calculate a Message Authentication Code (MAC) for each TCP segment
    Use MD5 to calculate MAC
    Calculate MAC over the TCP segment and the pre-shared key
  Include an MD5 Signature Option in each segment
    MD5 Signature Option includes MAC
Receiving node procedures
  Calculate a MAC for each received TCP segment
  Discard the packet if the calculated MAC does not match the received MAC

## Slide 5: TCP-MD5 is deprecated
New requirements
  Change pre-shared keys without resetting TCP session
  Support multiple authentication algorithms
Pre-shared key change
  It is difficult to change TCP-MD5 pre-shared keys without resetting the TCP session
  It is difficult to reset TCP sessions that support BGP
  Therefore, TCP-MD5 pre-shared keys were rarely changed
Authentication algorithm agility
  MD5 has been replaced by stronger authentication algorithms
  Even stronger authentication algorithms are expected in the future

## Slide 6: TCP-AO [RFC 5925] replaces TCP-MD5
Supports
  Pre-shared key change without resetting TCP session
  Multiple authentication algorithms

## Slide 7: TCP-AO Concepts
Master Key Tuple (MKT)
  One or more MKTs are configured on each node
  Used to derive traffic keys
Traffic key
  Used to generate a MAC for each TCP segment
TCP-Authentication Option
  Used to authenticate TCP segments
  Contains a MAC, KeyID and RNextKeyID
    KeyID identifies MKT and traffic key that were used to generate MAC
    RNextKey identifies MKT and traffic key that the receiving node should use when generating a MAC for the next segment it sends

## Slide 8: MKT Contents
A TCP connection identifier
  Source address, destination address, source port, destination port
  Wildcards allowed
A TCP Options flag (determine which TCP options are covered by MAC)
Identifiers
  Sending: Used to generate KeyID on outbound segments
  Receiving: Used to resolve KeyID on inbound segments
An authentication algorithm
Master key (i.e., keying material)
A key derivation algorithm

## Slide 9: Traffic keys
Four traffic keys are derived from each MKT
  SEND_SYN
  RECEIVE_SYN
  SEND-OTHER
  RECEIVE-OTHER

## Slide 10: The TCP Authentication Option
Message Authentication Code (MAC)
(Variable Length)
Kind=29
RNextKeyID
KeyID
Length
-

## Slide 11: Pulling it all together: Keying
Each node is each configured with one or more MKTs
Each node derives four traffic keys from each MKT
Each node independently determines which MKT is active
  Method is beyond the scope of RFC 5925
  Many implementations specify a start-time and an end-time for each MKT

## Slide 12: Pulling it all together: Authentication
Sending node procedures
  Calculate a Message Authentication Code (MAC) for each TCP segment
    Use the appropriate authentication algorithm
    Calculate MAC over the TCP segment and an active traffic key
  Include a TCP-AO in each segment
    TCP-AO Option includes MAC, KeyID and RNextKeyID
Receiving node procedures
  Calculate a MAC for each received TCP segment
    Use algorithm and traffic key associated with the received KeyID
  Discard the packet if the calculated MAC does not match the received MAC

## Slide 13: Relationship with GTSM [RFC 5082]
GTSM protects eBGP sessions
  Sender sets TTL to 255
  Receiver rejects packets containing eBGP if TTL is less than 254
TCP-AO still needed to protect eBGP sessions from attackers that are one hop away
TCP-AO still needed to protect iBGP sessions from internal attack

## Slide 14: Call to Action
Operators:
  Think about how TCP-AO fits into your overall routing security strategy
  Router vendor implementations are available now, start looking at them
  Ask for TCP-AO in RFPs/RFIs if it’s missing
Developers:
  There is no ecosystem of open source implementations and tools yet
  Need kernel implementations: Linux and *BSD
  Need features in routing implementations: BIRD, FRR, goBGP, OpenBGPD, etc.